## Slide 1
Data Logger using FreeRTOS on STM32
Viren Sharma-21UEC143 Kartik Khandelwal-21UEC071
Faculty mentor- Dr. Deepak Nair
1

## Slide 2
Project Overview and Design Goals
1
Goal
Build a real-time, accurate data logging system with low power consumption.
2
Design Goals
Efficient data collection from multiple sensors (RCWL0516, MQ135, RTC Module).
Real-time data display on an OLED screen.
Ensure synchronized access to shared resources using RTOS mechanisms (mutexes and semaphores).
Reliable data storage on an SD card with
timestamped entries.
Modular system architecture to facilitate debugging and future expansions.
2

## Slide 3
Components
RCWL-0516
A proximity sensor to detect human in the environment.
RTC Module
Provides accurate timekeeping, crucial for timestamping data.
OLED SSD1306
Provides a clear real-time display for visualization of collected data.
SD Card
Offers non-volatile memory for long-term data storage, ensuring data persistence.
MQ135
Air quality sensor for detecting gases.
STM32F446RE
Handles sensor data acquisition, data processing, and system control using RTOS.
3

## Slide 4
System Architecture
OLED Display
Display Task
STM32
Logging Task
Write Data to SD Card
RCWL-0516 Motion Sensor
MQ135 Sensor
Inbuilt-Real-Time Clock
I2C
Mutex
Digital
O/P
ADC
Mutex
SPI
CPU Core Temperature
DMA
ADC
Programmable
Switch
Interrupt
4
PC
UART
Binary Semaphore

## Slide 5
Proposed System
RCWL-0516
OLED
MQ135
SD card module
STM32 Nucleo
5

## Slide 6
How we utilized Mutex and Semaphore
Mutex: Ensuring Safe Resource Access
OLED Display:
A mutex ensures only one task can write to the OLED display at a time, preventing
conflicts and data corruption.
SD Card:
Same mutex synchronizes access to the SD card, ensuring that only one task
writes data at a time to avoid collisions.
Give and Take mechanism of mutex ensures that a resource such as the SD card
and OLED is not simultaneously accessed by multiple tasks.
Binary Semaphore
Switch Task:
1
2
Programmable switch task utilizes semaphore functionality to allow
interrupt functionality with FreeRTOS architecture. The semaphore is
preferred when utilizing the ISR functionality.
6

## Slide 7
Issues Encountered
Hardfault Issue: Our program entered hardfault due to memory overflow
in the task which upon debugging was altered. Stack size details were analyzed
using the CubeMX FreeRTOS task list, which was configured to monitor stack
utilization and identify potential overflows or memory mismanagement.
Priority of OLED task: The comprehensive breakpoint debugging approach
allowed in better understanding the data corruption on screen due to
simultaneous sending of data onto the OLED via various tasks. To avoid such
corruption mutexes were used.
7

## Slide 8
8

## Slide 9
FreeRTOS Task list
9

## Slide 10
SPI
10

## Slide 11
UART
11

## Slide 12
Segger
12

## Slide 13
Working
13

## Slide 14
SD Card Data
14

## Slide 15
1-15 September
Basic Code
16-30 September
Basic Code and Testing
1-15 October
Basic Code, Testing and Debugging
16-30 October
Testing and Prototyping
Testing, debugging, prototyping, final design and report writing
T I M E L I N E
31 October-15 November
16-30 November
Final design coding and testing, Final Submission
15

## Slide 16
Thank You
14